## Slide 1: Presentation Outline
1- Project description
2- HPLC method: preparation of standards, separation of metabolites, retention time
3- Analysis of glycerol samples:
3.1) Tech grade glycerol 3.2) Crude glycerol 3.3)Glycerol pitch
4- S.cerevisiae: pathway from glycerol to succinate
5- Y. lipolytica: pathway from glycerol to glyoxylate

## Slide 2: Project Description
Huge rise in the price of petroleum and environmental concerns
Biodiesel is an alternative with crude glycerol as a byproduct
Tremendous increase in the production of crude glycerol and huge decline in its price
Conversion of crude glycerol into valuable organic acids
Enhance economic viability of biodiesel industry

## Slide 3: Choosing Optimal HPLC Method
Retention time: Separation of important metabolites
HPLC Method: Eluent :5mM H2SO4,
Column temperature : 36C,
Flow rate :0.4ml/min,
Run time: 35min

## Slide 4: Interference of AKG-Malate-Pyruvate

## Slide 5: Standards: Glycerol

## Slide 6: Analysis of Glycerol Samples:
1) Technical Grade Glycerol : 91.51% glycerol
2) Crude Glycerol : 60.85% glycerol
3) Glycerol Pitch : 62.04% glycerol

## Slide 7: S. cerevisiae: Pathway from Glycerol to Succinate
Growth of S. cerevisiae (CEN.PK113-1A) on glycerol :
Wild Type : Low rate of growth, Low glycerol consumption
Negligible effect of temperature and amino acids on growth
No growth in anaerobic conditions on glycerol
significant amounts of biomass produced, low concentration of organic acids produced

## Slide 8: Effect of Amino Acids and Temperature on Growth

## Slide 9: Effect of Aeration on Growth

## Slide 10: Significant amount of biomass produced, low secretion of organic acids

## Slide 11: Metabolic engineering of S. cerevisiae
Substrate Utilization engineering:
Glycerol uptake from extracellular space: STL1(proton symporter) in plasma membrane
Glycerol transport inside Mitochondria:
GUT1-Glycerol Kinase
Introduction of Active transporter from other strains: P. tannophilus, Y. lipolytica, P. pastoris

## Slide 12: Cofactor Balance:
Most optimal pathway through reductive TCA cycle
Reductive route = essentially anaerobic
Not a significant amount of excess ATP
Transformation to verify whether the oxidative route yields succinate: ΔLSC2 mutant

## Slide 13: Growth of Wild and Mutant Type

## Slide 14: Glycerol Consumption of Wild and Mutant Type

## Slide 15: Y. lipolytica: Pathway from Glycerol to Glyoxylate
Higher growth rate of wild type (NRRL Y-423) and PO1f strains on Glycerol
Higher consumption rate of Glycerol by Y. lipolytica
Safe-to-use organism with literatures available (information about growth medium, genome sequence, transformation protocol, etc)
Secretion of the variety of organic acids/ metabolites especially citric and isocitric acid

## Slide 16: New HPLC method for separation of Glyoxylate, Pyruvate , AKG and Citrate
New pathway -> New metabolites -> Revision of HPLC method to separate glyoxylate, AKG and pyruvate
Separated metabolites with the aid of HPLC optimizer
New conditions given the constraints:
- Eluent: 10mM H2SO4
- Flow rate: 0.3ml/min
- Column Temperature: 36C
- Run time: 30min

## Slide 18: Verification of citric acid production from PO1f and NRRL Y-423:
Bioprocess Optimization: While growth conditions such as nitrogen source are limited and there is high concentration of carbon source(carbon shock) the cells tend to produce higher amount of citric acid.
Citric Acid Producing Medium(MP): YNB with 1g/L ammonium sulphate + 5% Glycerol
Growth Medium(MG): YNB with 3.5g/L ammonium sulphate + 2% Glycerol

## Slide 19: No citric acid produced from PO1f strain: 1) MP Glycerol 2) MG Glycerol

## Slide 20: 1) MP Crude 2)MG Crude

## Slide 21: 1)MP Pitch 2)MG Pitch

## Slide 22: Growth on Glycerol and Glycerol Consumption of PO1f strain

## Slide 23: Citric acid produced from NRRL Y-423 strain: 1)MP Glycerol 2)MG Glycerol

## Slide 24: 1)MP Crude 2)MG Crude

## Slide 25: 1)MP Pitch 2)MG Pitch

## Slide 26: Citric acid Production in MP and MG Media

## Slide 27: Growth on Glycerol and Glycerol Consumption of NRRL Y-423 Strain:

## Slide 28: Citrate to Glyoxylate:
Citrate -> Isocitrate:
ACN(aconitase) overexpression
isocitrate -> Glycolate:
ICL (isocitrate lyase) overexpression
Glycolate -> Glyoxylate: YcdW (glyoxylate reductase) overexpression from E.coli GLYR1
glyoxylate ->malate: Malate synthase deletion

## Slide 29: Separation of citrate and isocitrate
Using enzyme-based assay:
1)The enzyme isocitrate dehydrogenase is added to a solution of isocitrate.
2)The concentration of NADP+ obtained at 450nm after 30mins
3)Rate of NADP production versus the known concentration of substrate(isocitrate) is used as standard curve for measuring isocitrate concentration

## Slide 30
To do:
Test the separation of isocitrate and citrate
Toxicity level of glycolate on Y. lipolytica
The effect of Malate synthase deletion, CAN, YcdW and ICL1 overexpression on isocitrate and glyoxylate yield